## Slide 2
P074
Preliminary Vehicle dynamics simulations

## Slide 3: Peak speed and accelerations
Hypothesis
Weight balance 49% front
Vertical stiffnesses for 106 N/mm front, 116 N/mm rear
3rd elements tuned to engage above ~180km/h and limit ride height reduction with speed. (180 N/mm front, 120 N/mm rear)
3rd dampers 5000 N/(m/s)
Tires mu scaled to match target lap time (~3m 30s), +6% on the SCG003C tires model
Tires nominal load scaled linearly with width (hypothesis 13” (330mm) front, 15” (380mm) rear)
Results
Top speed about 330 km/h (residual longitudinal acceleration ~0.01g)
Maximum braking deceleration 2.8g
Maximum cornering 3.0g

## Slide 4: Fuel Consumption
Hypothesis
Tires performance tuned to match ~3m 30s lap time in Le Mans (30kg fuel, 50kg bop)
BSFC constant at 250 g/(kW/h), from worst working point of Honda for SCG003C being about 245 g/(kW/h)
Engine torque curve as per rules -1kW, times 1.05 (rules curve is specified at output shafts). Hypothesis of Nmax = 7000 rpm.
Gearbox efficiency 0.95
Gearbox ratios selected from Xtrac catalogue. Hypothesis of maximum power (6650rpm) at 325 km/h
Results
Varying the setup of the car and the weight distribution, a little variability is observed in results
Foreseen fuel consumption is between 8.99 and 9.23 liters per lap (about 110 liters per race)
Fuel density assumed 0.73 kg/l